## Slide 1: FoCal Readout and Trigger
K. Oyama
Nagasaki Institute of Applied Science
2nd International Workshop on Forward Physics and Forward Calorimeter Upgrade in ALICE, Tsukuba, JAPAN, 13, Mar. 2023

## Slide 2: FoCal PAD Readout Scheme (review)
Developments finished by Grenoble
Picture from draft paper “Prototype electronics for the silicon pad layers of the future Forward Calorimeter (FoCal) of the ALICE experiment at the LHC”, O. Bourrion et al.
1/22 of entire FoCal
5 HGCROCs on one board (5 x 72=360 pads)

## Slide 3: FoCal PAD Readout Scheme (review)
An aggregator FPGA processes data from four 5-pad boards (20 HGCROCS)
  zero suppression & formatting
  trigger sum
  control
GBT
GBT
FPGA
20 HGCROC connected to a FPGA
40 eLinks for Data
40 eLinks for Trigger Sum
aggregator
Picture from draft paper “Prototype electronics for the silicon pad layers of the future Forward Calorimeter (FoCal) of the ALICE experiment at the LHC”, O. Bourrion et al.
HGCROC data b.w. (1.28 Gbps x 40=51.2 Gbps) is compressed and sent by 2 GBT links (3.2 Gbps x 2) by:
trigger (up to 200-500 kHz)  32bit x 72ch x 20 HGCROCs x 500 kHz = 23 Gbps
zero suppression (1-12%, avg. < 10%)  2.3 Gbps … ok for up to ~25% avg. occupancy

## Slide 4: Pad Readout Scheme (questions)
Concerns during prototype developments
FPGA in radiation area
  If not, then there are several solutions
    replacing aggregator FPGA with ASIC (either existing ASIC or develop ourselves)
    choose rad-hard FPGA and implement simpler logic
    put the aggregator away (~5m) from the detector and pull copper cables
Can we readout for higher occupancy than 10% (such as pA) at 500 kHz? Similarly, can we readout pp at min.bias (1 MHz) for pad?
  Switch to lpGBT (10.24 Gbps) gives 3 times higher b.w.
  HGCROC data at 1 MHz pp  32bit x 72ch x 20 HGCROCs x 1 MHz x 10%= 4.6 Gbps … OK!
  With one lpGBT max. tolerated avg. occupancy is 10.24/46 = 22%
  We don’t need to stick on grouping of 4 layers  (example) one lpGBT per 3 layers  30% is tolerated
  There is no reason not to use lpGBT anywas because it’s a next standard to GBT at CERN experiments
https://japan.xilinx.com/products/silicon-devices/fpga/rt-kintex-ultrascale.html#radiation

## Slide 5: PAD readout concerns (summary)
Present development by Grenoble + switch to lpGBT
  radiation concern
  rad-hard FPGA(minimum function) + SCA  ok
put aggregator away
  Signal integrity problem with long 3960 copper cables for 1.28 Gbps to be solved
Introduce ASIC for data reduction and trigger sum
  CMS ECON-D and ECON-T ASICs are candidates?
  Original ASIC  long development time?
  Not very high advantage in case of ECON-D compare to (d) in terms of number of lpGBTs
    With our own ASICs, it can be similar to (a)
No FPGA nor ASIC for aggregation but use only lpGBT
  Many optical fibers and many CRUs
Additional FPGA for (c) and (d) can be considered to reduce number of CRUs but may not give advantage in terms of cost
Rad-hard
FPGA
CRU
~100 m 88 (=22x4) lpGBT fibers
(or 132 (=22x5))
<50 cm
3960 eLINK traces
Aggregator2
5 CRU
FPGA
CRU
~100 m
88 lpGBT fibers
>5 m
3960 eLINK long cables
(needs buffer in between?)
Aggregator1+
5 CRU
ASIC
CRU
<396 lpGBT fibers
17 CRU
<50 cm
3960 eLINK traces
(a)
(b)
(c)
CRU
min. 660 lpGBT fibers
28 CRU
<50 cm
3960 eLINK traces
(d)
Lp GBT
Lp GBT
Lp GBT
Lp GBT
FPGA?
FPGA?
this is what TPC took, with GBT-SCA for slow control
~100 m
~100 m
numbers can be smaller depending on ASIC design

## Slide 6: Using ECON-D and ECON-T ASICs?
https://indico.cern.ch/event/818783/contributions/3598486/attachments/1950405/3237629/HGCAL-CHEF19-FS.pdf

## Slide 7: ECON-D
Basic use case by CMS: 12 eRX  6 eTX  1 LpGBT
However, it is also possible to enable/disable individual eTX according to data amount
  Using two eTX is is safe (keep one as option)
    eLink reduction factor is 122(6) or 102(5) depending on our layout
  Necessary number of lpGBT is either 3960/5/6=132 (6 CRU) or 3960/6/6=110 (5 CRU)
Data reduction by
  zero suppression (auto-corrected threshold)
All configuration through by GBT SCA
use only one or two For FoCAl

## Slide 8: Possible readout scheme with ECON-D
To use full channels, 12 channels (6 HGCROC) is into one ECON-D is the best
  since we have 18 layers, 3 layers x 6 groups is the best
  but routing in Z direction is maybe not trivial
Maybe the most natural is one layer for one ECON-D
ECON-D
unrealistic
Aggregator2
ECON-D
ECON-D
lpGBT
SCA
fiber to CRU
3 full layers read out by a single lpGBT … maybe this is the best with enough safety margin
other option is to read out 6 layers by a lpGBT if it is really safe in terms of occupancy
short distance
through Grenoble style Interface Bard
short
distance
6 lpGBT per module
6x22=132 lpGBT for FoCal

## Slide 9: Trigger
HGCROC maximum trigger rate: 1 MHz (sustained average)
  It has long enough buffer  latency of CTP trigger is no problem
ALPIDE (Pixel) trigger rate is limited
  It has only three event buffers inside, and no busy output (busy protection impossible)
    Avoid busy violation by limiting individual readout rate of each strip
    Busy violation flag is available  RU may detects and put in data stream
    Assumption is that we limit readout rate to ~100 kHz (system-C simulation by Max will give us more precise and safe number) … see Dieter’s presentation
    Timing of trigger to ALPIDE is crucial (CTP LM)

## Slide 10: ALPIDE requirements for triggered mode
ITS2 requires LM (Level minus one, designed for TRD) arrival at ~1.2 s
  distribution via CRU doesn't fulfill the timing requirement (2.3 s)
  ITS2 took solution to directly send CTP LM to sensor through the RU
  for details please see below (thanks Johan for providing this)
    https://indico.cern.ch/event/580057/contributions/2382306/attachments/1390715/2135376/WP10_EDR_Timing_v6.pdf
    https://indico.cern.ch/event/580057/contributions/2382324/attachments/1394559/2131547/WP10_EDR_trigger_distribution_v3.pdf
in FoCal case, we need to carefully think about how to trigger PIXEL by which trigger detector
  only FIT will contribute to LM … only hadronic
  UPC physics needs ZDC as trigger input but ZDC can’t do LM
  FoCal self trigger is only solution?
  what’s other physics?

## Slide 11: ALPIDE pile-up
Event interval at 1 MHz min. bias operation can be below 1 s (40 BC)
Events from other interaction overlap in given ALPIDE data
1.2 s
c
trigger
c
ALPIDE
HGCROC
For the second event, first and second events overlay, and we have no way to distinguish
 we can flag or reject
pad
We can associate and remove green signals from red events
(better we know green is there in offline)
R
R

## Slide 12: Past-future protection at pad level
At trigger level, we can reject events with large overlap of physics signals in the same pad
c
c
ALPIDE
HGCROC
Clean event without any problem
Event highly contaminated with past and future events
At trigger level we can reject those events or put a flag (raw data stream)
CTP “may” reject events. So, we need to handle this at trigger processor

## Slide 13: ALPIDE triggering idea
GLOBAL trigger for all PAD, HCAL and PIXEL
  PAD and HCAL are fully read out with this (up to 1 MHz depending on Aggregator design)
ROI (region of interest) mask additionally for PIXEL
  only strips with condition (GLOBAL && ROI) == 1 are read out (max rate: < 100 kHz)
global trigger using Pad and Hcal
for physics selection
(layers to use can be selected with wiring and FPGA programming)
ROI
at very low threshold
only pixel strips with signal in HGCROC at front and back (or few more if needed) are readout
necessary granularity has to be studied

## Slide 14: Trigger very basic concept
FPGA based trigger processor for analyzing HGCROC trigger stream
  GLOBAL: to CTP as L0 contribution input (min.bias, 0, , jet, UPC, …)
  pretrigger: GLOBAL && ROI mask information only for PIXEL
  Datastream for trigger and past-future information
Pad (&HCal)
(HGCROCs
and SCA)
CRUs
FoCal Trigger Processor
(large FPGA or 2 stages FPGAs)
PIXEL
CTP
LTU
HGCROC trigger stream
(selected lines)
4 pad layers  880 eLinks
or already aggregated data
RU
GLOBAL
L0 contrib.
LVDS Coax.
individual strip r/o trig.
rate < 100 kHz @ 1.2 s
 HGCROC r/o trig. <1 MHz @ >1.6 s + CTRL
 data stream
to other ALICE detectors
pretrigger = GLOBAL && ROI
 CTRL
 data
 trigger + CTRL
 data
 trigger + CTRL
 data
to DAQ

## Slide 15: ECON-T
CMS trigger requirement: L1 at 750 kHz, 12.5 s latency
ALICE (ALPIDE) trigger requirement: pre-trigger at 1.2 s latency
ECON-T super trigger cell algorithm latency is 300 ns … good!
Port use is selectable, depending on algorithm to use
We need measurement and simulation
Note:
HGCROC fast control is directly from lpGBT and slow control of everything is using SCA
  no extra clock recovery (PLL)
ALICE TPC (with SAMPA) also has the same concept (and working well)

## Slide 16: ECON-T
Super trigger cell (STC) algorithm is similar to what we are thinking for FoCal

## Slide 17: ECON-T
STC16 (16 TC into one sum): 16x7 bits  4E+3M+4A(11 bits)
  reduction factor of 11/112 ~ 0.1
  might be possible 12 eRX into 2 eTX (careful check needed)
  assuming so:
    we can reduce 3960 HGCROC trigger outputs eLinks to 660 eLinks
    Since latency is low, maybe we can collect them using lpGBT
      660/6 = 110 lpGBT
      We may not connect “entire” pad layers assuming only 4 layers (4/18), 110 can be reduced to 25 lpGBTs
        feasible to inject into one FPGA for trigger processor
        but we loose charge collection statistics and energy resolution if we want to trigger for shower or jet
        for min.bias trigger, it might be ok

## Slide 18: Layout consideration with ECON-T
STC16 (16 trigger cell into one sum)
  1 HGCROC has 8 trigger cells  SRC16 perform two HGCROC into one sum
  two HGCROCs in the same tower is better for also to keep position granularity in trigger algorithm (pattern b instead of a)
  a group has 2 layers instead of 3 layers for ECON-D
Need to check with pixel
  IB configuration 3 ALPIDEs corresponding to 1 HGCROC geometry can be triggered individually
?
pad
****
trigger
cell (STC)
trigger cell
HGCROC
(a)
(b)
to the same ECON-T

## Slide 19: Aggregator ver.2 with FPGA?
Replace ETH for controlling and monitoring with GBT SCA
Replace GBT with lpGBT
Limit function of FPGA for to reduce radiation cross section
Add function to recover FPGA configuration during run

## Slide 20: Possible layout of Aggregator 2
for data reduction in FPGA, Grenoble development can be ported
less function  smaller PCB
lpGBT optical through firefly?
FPGA
(R.T. or Normal)
or
ASIC
GBT
SCA
lpGBT
lpGBT
lpGBT
data
trigsum
FPGA
(R.H.)
trig&CTRL
slow control I2C
data
(30 eLinks)
trigger sum
(30 eLinks)
(re-)configuration
trigger/clock/fast control
6 eLinks
6 eLinks
x6 for a module
x6 x22 for whole FoCal
(fiber)
(fiber)
(fiber)
Aggregator 2
VReg.

## Slide 21: To do as summary and comparison
Aggregator ver.2 design … we may go with keeping different solutions
ECONs
  obtain and evaluate ECON-T first then ECON-D, probably with Saga setup?
    300 ECON-T packaged available … some can be given to ALICE
    ECON-T more production in a year and ECON-D production submission done
    (for final production, cost for wafer: $4600 for 200 chips  $2.4 /chip (+ packaging))
  detail discussion with CMS people and technical information transfer needed
  can’t expect full support for board design, debugging, operation
(rad-hard) FPGA
  investigation of rad-hard type or testing normal FPGA in radiation?
  other than that, the easiest and quickest solution
own digital ASIC
  VDEC framework of university of Tokyo can be used
  experienced people are there (Tsukuba, Saga, Nagasaki, and …)
  problems is development time
  not fully reconfigurable (except for parameters)
  very good to have this experience for our future experiments
  start prototyping by earning grant (its also investments for future)
no-aggregation
  cost? … we need anyways more FPGAs for trigger data collection and more CRU for data reception
Trigger processor
  design fully deepens on readout solution of pad
  looking for “many” input FPGA board
  test implementation of logic
  simulation of trigger performance

## Slide 22
backup

## Slide 23: Busy violation
ALPIDE has three “buffer depth”, w/o busy protection, data size depends on occupancy
too high trigger rate will cause busy violation (buffer full but received trigger)
preliminary result from Max https://indico.cern.ch/event/1166784/

## Slide 24: Detail trigger scheme (yet an idea)
advantage: full flexibility on choice of global trigger / ROI elements (matter of wiring and firmware)
EPad (&HCal)
5 tower mod.
90 HGCROCs
CRUs
FTP
(FoCal Trigger Processor)
PIXEL
trigger sum stream ~1280 bps x 180 links (wire, 5m)
data output stream
~1280 Gbps x 180 links (wire, 5m)
pre-trigger decision within 1200 ns
pre-triggered data
Local Trigger
Concentrator
Aggregator2
40
40
40
40
40
40
40
40
20
20
total max 4 x 10 = 40 Gbps
25 Gbps non SERDES link
(mult. wires, ?m)
from HCal
from
other 5 Epad
regions
not far from micro TCA crate, or in the same crate
from other 3 or 4 of 5-pad modules
(1/6 of total FoCal Epad)
micro TCA crate
CTP
LM contrib.
decision (bidir.)
pre-trigger decision within ~1000 ns
LTU
RU
ALICE trigger
Decisions
and timing
trigger and data (GBT bidirectional)
1-2 Gbps x 10 trigger sum
(wire <50cm)
no need to install all
FLP
trigger information to record
trigger
pre-trigger is
optional in case LM via CTP is too late
AND we run PIXEL with triggered mode
x4 HGCROC into one sum

## Slide 25: ALPIDE triggering idea
system-C simulation will soon tell us how often we can trigger ALPIDE safely
assuming ~100 kHz for pp is a safe limit
  GLOBAL physics triggers aggregated rejection factor of 5-10 will be safe with ROI
    assuming 3-5 different triggers, individual trigger may be required better than 10-20
additionally
  limit readout region for ALPIDE using HGCROC trigger stream  ROI: region of interest
  with enough low threshold on charge
  AND arithmetic with GLOBAL trigger
minimum ROI region size depends on PIXEL strip readout configuration
picture provided by Tea

## Slide 26: ALPIDE readout
supports triggered and continuous modes
continuous mode is equivalent to periodic trigger with long gate (ITS uses only this for physics)
  fake hits, noise and background (beam-gas) … needs study
  at FoCal, impossible to distinguish pile-up (minimum event interval can be much below 1 s)
triggered
continuous
(baseline)
S. V. Nesbo et al., “System simulations for the ALICE ITS detector upgrade”, EPJ Web of Conferences 245, 02011 (2020) https://bora.uib.no/bora-xmlui/bitstream/handle/11250/2731420/epjconf_chep2020_02011.pdf

## Slide 27
a
Si pad layer with
5 HGCROCs
Aggregator
GBT
20 HGCROC
40 eLinks for Data
40 eLinks for Trigger
GBT
FPGA
compressed data to
CRU (FPGA farm)
digested trigger data
to trigger processor (FPGA)
pad
****
trigger
cell (STC)
trigger cell
HGCROC

## Slide 28: Review: our present aggregator
One HGCROC has two 1.28 Gbps eLinks for data output
4 of 5-pad layer is to be readout by the aggregator
  20 HGCROC = 40 eLinks
  concentrated to 1 GBT of 3.2 Gbps
  wire reduction factor 1/40
  using LpGBT (10Gbps), it can be better than 1/100
  method: trigger, Z.S., and link speed
Similarly for trigger
Problem is radiation